## Slide 1
Received RF waveform
Reference interference
Detect & integrate
Intensity samples
Amplitude and phase
Known reference wave
Spatial interference pattern
Square-law energy sensing
Space × time
Pilot interval
Data interval
I Learn the channel
Pilot-guided direction and gain estimation
Pilot patterns
Refine directions
and path gains
Damped Gauss–Newton
Learned channel
Directions + gains
II Recover the baseband symbols
Reference-assisted phase retrieval
Data patterns
Predict intensity
Refine symbols
+
−
Reference-assisted GS
Use learned channel
Q
I
Resolved symbols
I
Q
I/Q symbol sequence
Notes: Source: main.pdf, Section II.B–D and Section IV.A–C, Algorithms 1 and 2. This is a conceptual signal-evolution illustration, not simulation or measured data. RF waveforms, energy envelopes, patterns, gain phasors and constellation points are schematic. The receiver interferes the incoming field with a known reference before element-wise square-law detection and subslot integration. Only intensity samples enter the digital algorithms. Stage I uses known pilots to initialize and refine DOAs and complex channel gains with damped Gauss–Newton; the learned channel is reused by Stage II. Stage II uses reference-assisted Gerchberg–Saxton alternating magnitude and finite-alphabet projections: add the known reference in the forward intensity prediction and remove it before back-projection. The cloud-to-constellation imagery depicts iterative constraint enforcement, not coherent I/Q mixing or an independent measured phase signal. The final I/Q traces represent the time-ordered detected complex symbols. No coherent RF downconversion is implied. QPSK is shown only as an illustrative finite constellation.