## Slide 1
A From symbols to RF
B Far-field propagation
C Holographic reception
Complex symbols
I
Q
Symbol sequence
Pulse shaping
I
Q
Overlapping pulses
RF modulation
I/Q carried by RF
Other users
Different arrival directions
Phase across the aperture
+
RIS interference
Square-law
Power detectors
Known reference wave
Added before
power detection
Zoom: one receiving element, one symbol
M = 4 subslots shown
One symbol interval, Ts
Subslot 0
Selected subslot m
Subslot 2
Subslot 3
t
Squared RF
at element i
Mean power
kTs
(k + 1)Ts
Δt = Ts/M
Integrate this area
One energy sample per subslot
Sample indexed at its midpoint tk,m
Retain the full pattern
Elements
Time / subslots
Symbol k
M Nr samples per symbol
Intensity-only observations
Notes: Source: main.pdf, Sections II.A, II.B and II.C, equations (1)–(8). This graphical model follows pulse-shaped complex symbols, RF modulation, far-field propagation, reference addition at the aperture and element-wise square-law energy sensing. Channel loss, shadowing and phase are absorbed into each complex path gain; directional phase varies across the array. The reference adds to the field before the power detector. The detailed lower plot uses a reproducible illustrative two-user raised-cosine waveform and a selected receive element, with a local reference. M=4 is drawn only for clarity. The selected m=1 window lies within symbol k=2. Each normalized integral gives one element/subslot energy sample, indexed by the subslot midpoint. All M samples per element and all Nr elements are retained; general pulse overlap requires block processing. The pale RF-squared ripple and its envelope energy are schematic in carrier scale; effective post-detection noise is omitted from the visualization. Optional transmit-side bias/pilot q(t) is omitted as allowed by xi=0. No coherent receiver I/Q mixing is implied.